## Slide 1: GPGPU Background
Hyesoon Kim

## Slide 2: CPU pipeline
CPU pipeline
Increasing the performance in the execution units
  Increase the issue width (superscalar)
  Multi-threading
Memory
Front-end
Decode
Rename
Schedule
Execution
Write-back
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
5-stage pipeline
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
Superscalar
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
Multi-threading

## Slide 3: GPU pipeline
Warp/Wave-front execution model
SPMD programming model (Single Program Multiple Data)
Inst 1
Inst 2
Inst 3
T1
Inst 1
Inst 2
Inst 3
T2
T3
T4
All threads have the same program
T
T
T
T
One warp
T
T
T
T
Fetch 1 instruction and each instruction has multiple threads are associated.
The group of instruction is called warp/wave-front
Tn
…
T
T
T
T
One warp
T
T
T
T

## Slide 4: GPGPU Programming
Become popular with CUDA (Compute Unified Device Architecture)
CUDA (Based on Nvidia architectures)
  Portland Group Compiler supports CUDA  x86
OpenCL

## Slide 5: Quick Summary of CUDA Programming Model
SIMD or SIMT
  Single instruction multiple data or single instruction multiple thread
Unified Memory space (global memory space)
Program hierarchy
  Thread, block, kernel

## Slide 6: Execution Model
Thread & Block
Inst 1
Inst 2
Inst 3
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
SM
SM
Shared Memory
SP
SP
SP
SP
Shared Memory
SP
SP
SP
SP
Block
Kernel
Block
warp
warp
warp
Sing instruction multiple thread
Block = a group of thread which share “the shared memory space”
Warp
warp
warp
warp
[the slide is from Hong&Kim ISCA’09]

## Slide 7: Memory Data Indexing
SIMT-execution model
Use thread id and block id to index data
Let’s assume N=16, blockDim=4  4 blocks
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
blockIdx.x = 0
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 0,1,2,3
blockIdx.x = 1
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 4,5,6,7
+
blockIdx.x = 2
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 8,9,10,11
blockIdx.x = 3
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 12,13,14,15
+
+
+
+

## Slide 8: 1D, 2D, 3D data structures
A kernel is executed as a grid of thread blocks
Threads and blocks have IDs
  So each thread can decide what data to work on
  Block ID: 1D or 2D
  Thread ID: 1D, 2D, or 3D
Loop index in sequential loop
  Use thread ids, block ids
  1D array index= c1*threadId.x + c2*block Id.x
  2D array index = c1*threadId.x+c2*blockId.x+c3*threadId.y+c4*blockId.y
for (ii = 0; ii < 100; ++ii) {
C[ii] = A[ii] + B[ii];
}
// there are 100 threads
__global__ void KernelFunction(…) {
int tid = blockDim.x * blockIdx.x + threadIdx.x;
int varA = aa[tid];
int varB = bb[tid];
C[tid] = varA + varB;
}
CPU code
CUDA code

## Slide 9: Memory Space
 | Space | ~= CPU
Local Memory | Within Threads | Stack
Shared Memory | Within Blocks | Distributed memory space
Global Memory | All | Centralized storage
Constant Memory | All | Centralized read-only storage (very small)
Texture Memory | All | Centralized read-only storage (medium size, 2D- cache)
Thread, block, and kernel have different memory spaces

## Slide 10: CUDA Program Example

## Slide 11: Number of Threads Per CUDA Block
Host sets the number of threads per CUDA block. E.g., threadsPerBlock
Set up at the kernel launch time
# of registers per CUDA block
  Compiler sets how many architecture registers are needed for each CUDA block (Will be covered later part of the course)
  Typical CPU ISAs, # of registers per thread is fixed (e.g., 32), but in CUDA, this is flexible
Shared memory size is determined from the code
E.g., __shared__ int sharedMemory[1000];  4B*1000 = 4000B
kernelName<<<numBlocks, threadsPerBlock>>>(arguments);
Notes: Host sets the number of threads per CUDA block. E.g., threadsPerBlock when it launches the kernel.
# of registers per CUDA block can be varied.
  Why?
  Because the compiler sets how many architecture registers are needed for each CUDA block
  (This Will be covered later part of the course)
  Typical CPU ISAs, # of registers per thread is fixed (e.g. 32) but in CUDA, this is flexible
Shared memory size is also determined from the code
E.g., __shared__ int sharedMemory[1000];  4B*1000 = 4000B
So the occupancy is determined by these factors.

## Slide 12: Shared Memory
From: http://accel.cs.vt.edu/files/lecture10.pdf

## Slide 13: Synchronization Model
Bulk-Synchronous Parallel (BSP) program (Valiant [90])
Synchronization within blocks using explicit barrier
Implicit barrier across kernels
  Kernel 1  Kernel 2
  C.f.) Cuda 3.x
barrier
Block
barrier
Block
barrier
barrier
Block
barrier
Block
barrier
Block
Kernel1
Kernel2
Barrier

## Slide 14: OpenCL vs. CUDA
 | OpenCL | CUDA
Execution Model | Work-groups/work-items | Block/Thread
Memory model | Global/constant/local/private | Global/constant/shared/local + Texture
Memory consistency | Weak consistency | Weak consistency
Synchronization | Synchronization using a work-group barrier (between work-items) | Using synch_threads Between threads

## Slide 15: GPU Pipeline
Fetch
  One instruction for each warp
  Multiple PC registers exist to support multi-threaded architecture
  Round-robin scheduler
Wide execution width
Scheduler
I-cache
Fetch unit
Decoder
. . . . . .
Memory access unit
. . . . . .
Writeback
Memory
Lane 0
Lane 1
Lane N-1
Lane 0
Lane 1
Lane N-1
Active bit mask vectors/
score boarding
Register
Scheduler (Score boarding)

## Slide 16: GPU Register Files
To accommodate a large number of active threads, a large number of register files are essential.
e.g.) 128 threads, 64 registers = 128X64 = 8KB
NVIDIA G80 architecture: 64KB registers (16KB cache)
Vortex: 32x # of threads per warp x # of warps x # or cores
Register read BW
1Tflop/s peak performance (2 read, 1 write)
  -2T * 32B/s = 64TB/s register read BW
Highly banked register files

## Slide 17: Register File Structures: Multiple Banks
. . . . . .
. . . . . .
. . . . . .
Register files
. . . . . .
Lane 0
Lane 1
Lane N-1
Warp 0’s reg file
Warp M-1’s reg file
Warp ID.Reg ID
. . .
Th 0
…
Th N-1
Writeback
Multiple banks (Narasiman’s figure)
All threads in a warp read the register values in parallel.
Register is indexed with register ID, warp ID

## Slide 18: Handling Branch Instructions
A reduction example
What about other threads?
What about different paths?
0
1
2
3
4
5
6
7
0
2
4
6
0
4
0
If (threadId.x%==2)
If (threadId.x%==4)
If (threadId.x%==8)
A
B
C
D
If (threadid.x>2) {
do work B}
else {
do work C
}
From Fung et al. MICRO ‘07
Divergent branch!

## Slide 19: Split/Join
Compiler inserts split/join
Split:
  Put tmask in the ipdom stack (do work c part}
  Put next PC in the stack (not-taken path. // do work c part )
Join
  Pop from a stack
If (threadid.x>2)
// split
{
do work B
}
else {
// join
do work C
}

## Slide 20: How Many CUDA Blocks on One Stream Multiprocessor?
SM
SM
SM
Cache
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
SM
  How many CUDA blocks can run on one streaming multiprocessor?
  Multiple blocks per SM
Grid 0
Block (2,0)
Block (0,1)
Block (1,1)
Block (2,1)
2 to 1?
3 to 1?
Block (0,0)
Block (1,0)
Occupancy

## Slide 21: Occupancy
How many CUDA blocks can be executed on one SM is decided by following parameters
  # of registers, shared memory, # of threads
Exact H/W configurations are varied by GPU microarchitecture
E.g., HW: each SM can execute 256 threads, 64K registers, 32 KB shared memory
  SW: one CUDA block: 32 threads and 2KB shared memory and each thread has 64 registers
  Constrain by running threads: 256/32 = 8 CUDA blocks
  Constrain by register size = 64*1024/(64*32) = 32 CUDA blocks
  Constrain by shared memory = 32KB/2KB = 16 CUDA blocks
  Final answer: 8 CUDA blocks per SM
Notes: How many CUDA blocks can be executed on one SM can be decided by following: # of registers, shared memory, # of threads
Exact HW configuration are varied by GPU microarchitecture and different by each generation.
Let’s take a closer look at one example. We'll explore the example with 2 hundred 56 threads, 64KB of register files, and 32KB of shared memory.
In the software side, Each CUDA block has 32 threads and 2KB shared memory and each thread has 64 registers.
If the occupancy is constrained by running number threads, the total number of CUDA blocks per SM would be 256/32 = 8 CUDA blocks
If the occupancy is constrained by registers it will be 64*1024/(64*32) = 32 CUDA blocks
If the occupancy is constrained by shared memory it will be 32KB/2KB = 16 CUDA blocks
The final answer is the minimum of all constrains so the final answer is 8 CUDA blocks per SM

## Slide 22: Why Do We Care about Occupancy?
Higher Occupancy means more parallelism.
Utilization: Utilizing more hardware resources generally leads to better performance.
Exceptional cases will be studied in later lectures.
SM
SM
SM
SM
Block
Block
Block
Block
SM
Block
Block
SM
Block
Block
SM
Block
Block
Case (a): Each SM runs one CUDA block (6 threads per block)
Case (b): Each SM runs two CUDA block (4 threads per block)
SM
Block
Block
Notes: Why Does Occupancy Matter?
This is because higher occupancy means more parallelism.
Utilizing more hardware resources generally leads to better performance. <click>
In case (a) only one CUDA block runs on each SM and each CUDA block has 6 threads . <click>
In case (b) each SM can execute two blocks but each block has only 4 threads so total 8 threads per block which actually runs more threads than case (a)

## Slide 23: GPU Pipeline (1)
 | PC value
#1 (b:1, T1-T4) | 0x8000
#2 (b:1, T5-T8) | 0x8004
#3 (b:2, T1-T4) | 0x8000
#4 (b:2, T5-T8) | 0x800A
I-cache
Front-end
Decode
Memory
RF
Execution
Write-back
schedule
Shared Memory
0x8000 | add r1, r1, 1
0x8004 | sub r2, r,2,1
0x8008 | mov r1, tid.x
0x800A | mov r2, ctaid.x
0x8010 | ld.shared r1 [A]
tid.x: special register to store thread ID within a block
ctaid.x: special register to store block ID within a grid
 | Th1 | Th2 | Th3 | Th4
R1 | 11 | 12 | 13 | 14
R2 | 2 | 2 | 2 | 2
R3 | 3 | 4 | 13 | 15
R4 | 23 | 24 | 32 | 33
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
1
1
1
1
11
12
13
14
12
13
14
15
add r1, r1, 1
add r1, r1, 1
add r1, r1, 1
add r1, r1, 1
add r1, r1, 1
add r1, r1, 1
Notes: Here is a GPU pipeline
<click>
And here it shows PC values for each warp. In this example, there are 4 warps and the first warp should fetch from PC value 0x8000. and the first warp is from Block 1 and thread 1 to 4. The second warp is from block 1 as well and thread 5 to 8.
The 3rd warp is from block 2 and thread 1 to 4 and 4th warp is block 2 thread 5 to 8.
<click>
Here it shows register values for block 1
<click>
Here it shows an I-cache memory address and the instructions. <click>
You see tid.x at 0x8008. tid.x is special register to store thread ID within a block .
And an instruction at 0x800A has ctaid, which is another special register to store block ID within the grid
<click> Here is a scoreboard.
<click> The front-end fetches an instruction from 0x8000
<click>
Only one instruction for the entire warp.
<click>
And this one instruction is decoded in the decode stage.
<click>
Since the instruction has a constant value #1, the value is sent to all threads within a warp.
<click>
In the next stage, the processor access the register file and it reads r1 value form threads 1 to 4.
<click>
All source operands are ready <click>
So the scheduler selects warp 1 and then it will be executed <click>
The results will be written back <click> at the write back stage.

## Slide 24: GPU Pipeline (2)
 | PC value
#1 (b:1, T1-T4) | 0x8000
#2 (b:1, T5-T8) | 0x8004
#3 (b:2, T1-T4) | 0x8000
#4 (b:2, T5-T8) | 0x800A
I-cache
Front-end
Decode
Memory
RF
Execution
Write-back
schedule
Shared Memory
0x8000 | add r1, r1, 1
0x8004 | sub r2, r,2,1
0x8008 | mov r1, tid.x
0x800A | mov r2, ctaid.x
0x8010 | ld.shared r1 [A]
tid.x: special register to store thread ID within a block
ctaid.x: special register to store block ID within a grid
 | Th1 | Th2 | Th3 | Th4 | Th5 | Th6 | Th7 | Th8
R1 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
R2 | 3 | 3 | 3 | 3 | 2 | 2 | 2 | 2
R3 | 3 | 4 | 13 | 15 | 23 | 32 | 37 | 23
R4 | 23 | 24 | 32 | 33 | 11 | 7 | 8 | 5
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
1
1
1
1
2
2
2
sub r2, r2, 1
1
1
1
sub r2, r2, 1
sub r2, r2, 1
sub r2, r2, 1
sub r2, r2, 1
One lane is not shown
Notes: Now, let’s look at the 2nd warp.
It fetches an instruction from warp #2 which is block 1 and threads 5 to 8. <click>
Again the instruction is decoded. The constant value #1 is broad casted to all source operand buffers. <click> Here we omitted values for one execution unit due to the space limitation.
<click>
In the next stage, the processor access the register file and it reads r2 value form threads 5 to 8.
<click>
In this example all source values are all 2.
All source operands are ready <click>
So the scheduler selects warp 2 and then it will be executed Even those they are all operating the same values, the hardware performs the same work for all threads in a warp<click>
The results will be written back <click> at the write back stage just like the previous example.

## Slide 25: GPU Pipeline (3)
 | PC value
#1 (b:1, T1-T4) | 0x8000
#2 (b:1, T5-T8) | 0x8004
#3 (b:2, T1-T4) | 0x8000
#4 (b:2, T5-T8) | 0x800A
I-cache
Front-end
Decode
Memory
RF
Execution
Write-back
schedule
Shared Memory
0x8000 | add r1, r1, 1
0x8004 | sub r2, r,2,1
0x8008 | mov r1, tid.x
0x800A | mov r2, ctaid.x
0x8010 | ld.shared r1 [A]
tid.x: special register to store thread ID within a block
ctaid.x: special register to store block ID within a grid
 | Th1 | Th2 | Th3 | Th4 | Th5 | Th6 | Th7 | Th8
R1 |  |  |  |  |  |  |  | 
R2 |  |  |  |  |  |  |  | 
R3 |  |  |  |  |  |  |  | 
R4 |  |  |  |  |  |  |  | 
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
2
2
2
2
2
2
2
mov r2, ctaid.x
One lane is not shown
Block 2 register file
Notes: Now let’s assume the processor fetches from warp 4.
The PC address is 0x800A, which moves ctaid.x to r2.
The warp 4’s block id is 2, so ctaid.x value is also 2.
<click>
Ctaid.x value is read and stored inside the scoreboard.
<click> These values will be stored to R2 at the write back stage as shown in this animation.

## Slide 26: GPU Pipeline (4)
 | PC value
#1 (b:1, T1-T4) | 0x8000
#2 (b:1, T5-T8) | 0x8004
#3 (b:2, T1-T4) | 0x8000
#4 (b:2, T5-T8) | 0x8008
I-cache
Front-end
Decode
Memory
RF
Execution
Write-back
schedule
Shared Memory
0x8000 | add r1, r1, 1
0x8004 | sub r2, r,2,1
0x8008 | mov r1, tid.x
0x800A | mov r2, ctaid.x
0x8010 | ld.shared r1 [A]
tid.x: special register to store thread ID within a block
ctaid.x: special register to store block ID within a grid
 | Th1 | Th2 | Th3 | Th4 | Th5 | Th6 | Th7 | Th8
R1 |  |  |  |  |  |  |  | 
R2 |  |  |  |  |  |  |  | 
R3 |  |  |  |  |  |  |  | 
R4 |  |  |  |  |  |  |  | 
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
 | Src 1 |  | Src 2 | 
W1 | v | r | v | r
W2 | v | r | v | r
W3 | v | r | v | r
W4 | v | r | v | r
5
6
7
8
6
7
8
mov r2, ctaid.x
One lane is not shown
Block 2 register file
Notes: Now, let’s assume that instead of 0x800A, the processor fetches from 0x8008 for warp 4.
The instruction has tid.x since this is for threads 5 to 8, tid.x value will be 4,5,6,8,
The tid.x values will be read and stored in the score board.
<click> In the write-back stage, all these values will be written back to R1 as shown in this animation. <click>

## Slide 27: Mask Bits
What if we do not need to execute all 4 threads?
Mask bits tell which threads are active.
 | Src 1 |  | Src 2 | 
w1 | v | r | v | r
w2 | v | r | v | r
w3 | v | r | v | r
w4 | v | r | v | r
w5 | v | r | v | r
 | Src 1 |  | Src 2 | 
w1 | v | r | v | r
w2 | v | r | v | r
w3 | v | r | v | r
w4 | v | r | v | r
w5 | v | r | v | r
 | Src 1 |  | Src 2 | 
w1 | v | r | v | r
w2 | v | r | v | r
w3 | v | r | v | r
w4 | v | r | v | r
w5 | v | r | v | r
 | Src 1 |  | Src 2 | 
w1 | v | r | v | r
w2 | v | r | v | r
w3 | v | r | v | r
w4 | v | r | v | r
w5 | v | r | v | r
V
V
V
V
V
V
V
V
id | Mask bit
w1 | 1111
w2 | 1110
w3 | 0111
w4 | 1111
w5 | 1111
V
V
V
V
V
V
V
V
V
V
Notes: What if we do not need to execute all 4 threads?
GPU stores information tells which thread or lane is active.
<click> one ALU execution path is called lane.
Active thread performs actual computation and inactive threads will not do any work.
Mask bits tell which threads are active or not. <click>
Here scoreboard shows register values and ready bits.
Warp 1 has 1111 in the mask bits, <click> which means all threads in the warp1 will actually perform the work. <click>
warp1 is selected and <click> is executed.
In the warp 2 case, the mask bit is 1110 <click>. So only the first 3 lanes (or threads) will do the work. <click> <click>

## Slide 28: Summary
GPUs execute many threads as a group (warp/wave front)
GPU provides features to handle multiple threads concurrently and also time multiplexing
Massive thread level parallelism  massive memory level parallelsim