## Slide 1: Vortex Code Structure
Blaise Tine

## Slide 2: Agenda
Source Tree
Documentation
Hardware
Synthesis
Simulation
Runtime
Kernel
Testing and Integration
Configuration
Coding Convention
Debugging Vortex
Multi-threading

## Slide 3: Source Tree
Reference: /vortex
/ci: Continuous integration
/doc Documentation
/hw Hardware
/runtime GPU runtime
/kernel Kernel library
/sim Simulation
/tests Testing

## Slide 4: Documentation
Reference: /vortex/doc
Vortex.md
  Codebase Layout
  Microarchitecture
  Cache Subsystem
  Software
  Simulation
  FPGA Setup Guide
  Debugging

## Slide 5: Hardware
Reference: /vortex/hw
/dpi Verilog DPI library
/scripts Scripting tools
/syn Synthesis tree
/unit_tests Hardware unit tests

## Slide 6: Hardware - RTL
Reference: /vortex/rtl
/afu Command processor
/core Core components
/cache Cache source tree
/fpu Floating-point cores
/mem Memory system
/interfaces Module interfaces
/libs Library modules

## Slide 7: Hardware – Processor Dependency Tree
Vortex
socket
core
socket
socket
core
core
Mem_unit
sharedmem
icache
issue
fetch
decode
execute
commit
scheduler
ibuffer
scoreboad
operands
alu_unit
lsu_unit
fpu_unit
sfu_unit
dcache
L2 cache
cluster
socket
socket

## Slide 8: Hardware – AFU
Reference: /vortex/rtl/afu
opae: Intel OPAE
xrt: Xilinx XRT
OPAE
cci_to_mem
avs_wrapper
vortex
vx_to_mem
XRT
AFU
vortex
afu_ctrl
Notes: Xilinx Chipscope

## Slide 9: Hardware – Cache
cache
bank
bank_sel
tag_access
flush_ctrl
data_access
mshr
rsp_merge
nc_bypass
Reference: /vortex/rtl/cache
nc_bypass: cache bypassing
flush_ctrl: flushing
bank_sel: bank select
rsp_merge: response merge

## Slide 10: Synthesis
Reference: /vortex/hw/syn
/altera Altera FPGA synthesis
/xilinx Xilinx FPGA synthesis
/yosys Yosys synthesis
/synopsys Synopsys
/modelsim Modelsim

## Slide 11: Simulation
Reference: /vortex/sim
rtlsim: Processor RTL
vlsim: AFU RTL
simX: cycle-level

## Slide 12: Kernel
Reference: /vortex/kernel
/linker Loader scripts
/src Kernel API sources
  start.* Startup routine
  print.* Standard out print
  spawn.* Tasks scheduler
  perf.* Performance counter logger
  syscalls.* System calls handling

## Slide 13: Runtime
Reference: /vortex/runtime
/stub Stub library for linking
/opae OPAE FPGA runtime
/xrt XRT simulation runtime
/rtlsim RTL Simulation runtime
/simx SimX runtime

## Slide 14: Testing - Coverage
Reference: /vortex/tests
/kernel kernel tests
/regression C++ applications tests
/opencl OpenCL benchmarks
/riscv RISC-V conformance tests

## Slide 15: Testing - Integration
Reference: /vortex/ci
blackbox.sh Apps runner driver
regression.sh CI regression suite
Test_compiler.sh CI compiler suite
prebuild.sh Build prebuilt binaries
toolchain_install.sh Install prebuild binaries
Usage: <tool> --help

## Slide 16: Configuration - VX_config.vh
Reference: /vortex/hw/rtl/VX_config.vh
Contains all HW configuration parameters
  e.g. NUM_CORES, NUM_THREADS, L2_ENABLE
Autogen C++ header: VX_config.h
  $ make –s

## Slide 17: Configuration – VX_config.vh (2)
Startup
Memory
  IO
  COUT
  SMEM
Caches
  Enable/disable

## Slide 18: Configuration – VX_config.vh (3)
Cache config
  Banks
  MSHR size
  Queues sizes

## Slide 19: Configuration – VX_types.vh
CSRs
  Control status regs
  Performance counters
DCRs
  Device config regs
  Perf monitor class
  Startup location

## Slide 20: Configuration - Simulation
Reference: /vortex/hw/VX_config.h
  Auto-generated
Consumed by all SW components
  Vortex kernel library
  Vortex runtime
  All simulators
Blackbox examples:
  ./ci/blackbox.sh --cores=2 --warps=2 –app=vecadd
  CONFIGS=“-DNUM_CORES=2 -DNUM_WARPS=2“ ./ci/blackbox.sh --app=vecadd
  CONFIGS="-DMEM_LATENCY=100“ ./ci/blackbox.sh --app=vecadd

## Slide 21: Configuration - Synthesis
Reference: /vortex/hw/syn/opae
FPGA build scripts allows customization
  Use parameters from VX_config.vh
FPGA synthesis examples:
  CONFIGS="-DNUM_THREADS=4“ make fpga
  CONFIGS="-DNUM_WARPS=4“ make fpga
  CONFIGS=“-DPERF_ENABLE=4“ make fpga

## Slide 22: Coding Convention – Naming
Benefits of coding standard
  Self-documentation
  Refactoring
  Extensibility
Module files: VX_<module>.sv
Interfaces: VX_<interface>_if.sv
Header: VX_<name>.vh
Data Types: VX_<name>_types.vh

## Slide 23: Coding Convention - Interfaces
Reference: /vortex/hw/rtl/interfaces
Grouping of related signals
Master/slave interconnect
  Master: outgoing
  Slave: incoming

## Slide 24: Coding Convention – Handshaking
Elastic Pipeline Pattern
valid/ready interfaces
  out: data Data to transfer
  out: valid Producer has valid data to transfer
  in: ready Consumer is ready to accept data
fire => valid && ready;

## Slide 25: Debugging Vortex - Modes
Three debugging modes
  Cycle-Level Debugging
    Using Simx simulator
  RTL Debugging
    Using RTLsim or OpaeSim simulators
  FPGA Debugging
    Proprietary scope analyzer (Altera)
    Xilinx ChipScope (Xilinx)

## Slide 26: Debugging Vortex - SimX
When to use this mode?
  User application debugging
  Vortex S/W stack debugging
  New SimX extension
Example: debug levels=3
  $ blackbox.sh --driver=simx --app=demo –debug=3

## Slide 27: Debugging Vortex – SimX (2)
Generated output: run.log
  Instructions trace
  Fetched instruction
  Source operands
  Destination result
  Memory trace
  Stalls with info

## Slide 28: Debugging Vortex - RTL
When to use this mode?
  RTL code debugging
Command lines
  $ blackbox.sh --driver=rtlsim --app=demo –debug=1
Controlling debug trace via Makefile
vortex/sim/rtlsim/Makefile

## Slide 29: Debugging Vortex – RTL (2)
Generated output: run.log
  Instructions trace
  Fetched instruction
  Source operands
  Destination result
  Memory trace
  Stalls with info
Waveform: trace.vcd
  Detail is controllable
    Using Verilator annotation
vortex/sim/rtlsim/Makefile

## Slide 30: Debugging Vortex - FPGA
When to use this mode?
  FPGA debugging
  The EDA tool lacks a logic analyzer
Synthesis
  $ CONFIGS=-DSCOPE=1 make fpga-4c
Runtime
  $ blackbox.sh --driver=fpga --app=demo –scope
Generated Output: trace.vcd

## Slide 31: Debugging Vortex - UUID
Universal Unique Identifier
  Static number across runs
  Track instruction life cycle
    From fetch to commit
  Compare traces
  Compare RTL with SimX
RTL Trace
Simx Trace

## Slide 32: Debugging Vortex – CSV trace
Driver-independant Trace
  uuid
  PC
  opcode
  core_id
  warp_id
  tmask
  operands
  destination

## Slide 33: Debugging Vortex – CSV trace (2)
Comparing RTL vs SimX
  $ ./ci/blackbox.sh --driver=rtlsim --app=demo --debug=3 --log=run_rtlsim.log
  $ ./ci/trace_csv.py -trtlsim run_rtlsim.log -otrace_rtlsim.csv
  $ ./ci/blackbox.sh --driver=simx --app=demo --debug=3 --log=run_simx.log
  $ ./ci/trace_csv.py -tsimx run_simx.log -otrace_simx.csv
  $ diff trace_rtlsim.csv trace_simx.csv

## Slide 34
Thank You!