## Slide 1: Vortex Software Stack
Shinnung Jeong
Notes: Good afternoon. My name is Shinnung Jeong.
I am here today to provide you with an informative presentation on the Vortex software stack.
I will specifically focus on how this stack enables the launch of GPU programs on Vortex hardware.
Furthermore, I will introduce you to the OpenCL software pipeline.

## Slide 2
Vortex Software Stack
PoCL for the Vortex
LLVM compiler extension
Agenda
Notes: The agenda looks like this.

## Slide 3
__kernel void foo(){
tid = get_global_id(0);
…
barrier(…);
}
__host int main(){
…
cl_mem A_clmem = clCreateBuffer(context, …); clEnqueueNDRangeKernel(command_queue, foo, …); …
}
GPU Application (OpenCL, CUDA … )
Big Gap
Vortex GPU
Running a program binary of Vortex ISA extension
Runtime information is stored in the Vortex Control and status registers (CSRs)
Low level Driver for controlling Device
Comprising kernel and host code
Accessing runtime information and controlling program flow
Facilitating communication with the Vortex GPU
Motivation
Notes: People use GPU programming languages to develop GPU applications.
Many individuals employ languages like OpenCL and CUDA for writing their applications, and numerous applications have already been developed using these languages.
These two languages divide the program into two parts: code for the kernel and code for the host.
Kernel code requires access to runtime information, such as global IDs in OpenCL or thread IDs in CUDA.
kernel code also requires controlling program flow, including barriers and terminating executions.
On the other hand, host code needs to establish communication with the Vortex GPU, specifying commands for actions such as kernel launches and memory allocation.
Therefore, we require two types of methods: the first for accessing runtime information and controlling program flow, and the second for communication with the device.
On the Vortex side, programs must be written in Vortex ISA, not RISCV or any other instruction set.
Runtime information is stored in their local control and status registers.
Vortex uses the opae driver to configure, enumerate, open, and access FPGA accelerators.
However, there remains a significant gap between the programmer's code and the access to runtime information and communication.

## Slide 4
GPU Kernel
Kernel Compilation Stack
Vortex Kernel library
Target Codegen Compiler
Vortex Program
Program Execution Stack
Language-specific Runtime library
Vortex Runtime library
Language-specific Compiler
Overview of the Vortex Software Stack
Notes: To bridge the gap between the GPU and the code, we have implemented a software stack.
This is the Overview of the vortex software stack, which comprises two distinct components: kernel compilation into the Vortex binary and program execution.
The GPU kernel is defined using languages such as OpenCL or CUDA.
Our process begins with the analysis of program semantics and the generation of intermediate representation (IR) for the program.
Subsequently, we link with libraries that contain pre-built kernels for accessing runtime information and controlling program flow.
Lastly, we generate target code that consists of Vortex ISA instructions.
The program execution stack is also defined by specific programming languages.
In this case, we link function calls to methods that align with Vortex operations, such as Vortex memory allocation.
The Vortex runtime library contains essential information for communicating with the Vortex hardware.

## Slide 5: Vortex ISA Extension
ISA Extension of RISC-V ISA to support the Vortex GPU
  Wavefront Activation
    vx_wspawn %numW %func_ptr
  Thread mask activation and Active thread modification
    vx_tmc %tmask, vx_pred %cond %tmask
  Control flow divergence and reconvergence
    vx_split %pred, vx_join %stack_ptr
  Wavefront synchronization
    vx_barrier %barID %numW
A
B
C
D
If (threadid.x<2) {
work B
} else {
work C
}
Example Kernel
Control Flow Graph
Start
vx_join
vx_wspawn
vx_split
vx_join
Notes: Now, I will provide a more detailed introduction to the libraries and ISA extensions of the Vortex.
In order to support GPU operations, we have extended the RISCV ISA.
Since GPUs follow a SIMT (Single Instruction, Multiple Threads) architecture, it is important to have an ISA that can effectively control operations in SIMT architecture.
vortex use terminology wavefront and thread.
A wavefront is a group of thread and threads within one wavefront are executed in parallel and in lock steps.
The Vortex ISA introduces instructions for wavefront activation, allowing the launch of a kernel across a specified number of warps with a function pointer.
To manage threads within a warp, we introduce two ISAs, namely vx_tmc and vx_thread. These ISAs are responsible for activating and altering the active threads.
One of the most important aspects of the Vortex ISA is the introduction of split and join instructions to handle control divergence.
For instance, consider the code snippet in the top-right corner, which executes "work b" when the thread ID is greater than 2, otherwise, it runs "work c."
This code can lead to control flow divergence like bottom right figure.
To address control flow divergence in vortex, the split instruction pushes information about the current state of the thread mask into a hardware-immediate post-dominator (IPDOM) stack.
Subsequently, the join instruction retrieves this information during reconvergence.
Additionally, we have incorporated instructions for synchronization purposes.

## Slide 6: Vortex Kernel Library
Interface for accessing runtime information and controlling program flow
  Schedule a task on the parallel H/W?
    void vx_spawn_tasks(int num_tasks, vx_spawn_tasks_cb callback, void * arg)
  Query hardware specifications
    vx_num_cores(), vx_num_warps(), vx_num_threads()
  Query the current thread or wavefront
    vx_thread_tid(), vx_warp_id()
  Terminate program execution
    vx_tmc();
  Debug print to the console
    vx_printf(format, …);
  Other utility APIs
Notes: The Vortex kernel libraries consist of a set of kernels designed for running applications on the Vortex hardware.
In order to retrieve information and query hardware status, we require an interface, called vortex kernel library.
This vortex kernel library needs to be provided during kernel compilation.

## Slide 7: Vortex Runtime Library
Interface for communicating with the Vortex device
  Perform memory-related operation?
    vx_copy_to_dev(…), vx_copy_from_dev(…), vx_mem_alloc(…), vx_mem_free(…)
  Launch Kernel?
    vx_start(…), vx_ready_wait(…)
  Open and Close Device?
    vx_dev_open(…), vx_dev_close(…)
  Other Runtime Methods
Notes: For host code, certain fundamental operations must be implemented for communicating vortex and host CPU.
These operations include memory copying, memory allocation, and kernel launching, and all of these functions should be incorporated into the Vortex Runtime library.

## Slide 8
Kernel Code
(IR)
Built-in Library
(e,g. math functions)
Kernel executable
Vortex ISA
Front-end compiler
Back-end compiler
Analyze program semantics
Lower functions with built-in library
Lower IR to Vortex ISA using Vortex intrinsic
Perform vortex-specific optimization
Vortex
Kernel library
Host
Executable
Compiler
Lower device communication functions with runtime library
Vortex Runtime
Host Code
Kernel Code
Overview of the Vortex Compilation Flow
Notes: Now, I would like to provide a more detailed explanation of the Vortex compilation flow.
Compiler receive kernel code and host code as a input of compiler pipeline.
The kernel code undergoes initial analysis of program semantics through the front-end compiler, resulting in the generation of intermediate representation (IR). During this process, some functions are lowered using built-in libraries is performed.
Subsequently, the generated IR is transformed into a kernel executable by the backend compiler.
In this phase, the Vortex ISA is employed, and the Vortex Kernel library is linked.
On the other hand, the host code is responsible for creating the host executable through linkage with the runtime library.

## Slide 9
Command
Queue
DeviceMemCopy(…)
Front-end runtime library
Vortex Runtime Library
Vortex Host interface
Vortex accelerator Interface
Vortex Processor
External
Bus
Internal
Bus
Execution
Command
Host
Vortex GPU
Overview of the Vortex Execution flow
Notes: Now I will introduce the Vortex execution flow.
The commands required for device communication, as outlined in the host code, adhere to the following execution sequence:
First, they are linked with the frontend runtime library.
The frontend runtime library outlines how frontend methods can be executed using the Vortex runtime library.
The Vortex library carries out the operation using the Vortex host interface.
Vortex host interface, in turn, performs the operation on the Vortex processor, which is connected to the external bus via the Vortex host interface.

## Slide 10: Overview of the Vortex Software Stack
CuPBoP
Vortex Binary
vortex
Supporting laungague
  OpenCL (v3.0)
  CUDA (v10.1)
Frontend compiler
  Portable Computing Language (PoCL)
    Extension of PoCL v4.0
  Cuda for Parallelized and Broad-range Processors(CuPBoP)
Common Component
  RISCV toolchain (gcc, build_utils, etc)
  LLVM vortex
    Extension of LLVM 16
Open-GPU owned
repositories
Modified repositories
Notes: The Vortex software stack provides support for two different programming languages: OpenCL and CUDA. Currently, we offer support for OpenCL 3.0 and CUDA 10.1.
To enable support for these two languages, we use the Portable Computing Language (PoCL) and CUDA for Parallelized and Broad-range Processors.
We have extended the PoCL open-source repositories to ensure compatibility with Vortex and have implemented our own project called CupBoP.
As our backend compiler, we utilize LLVM, specifically an extended version 16. To fully support the entire software stack, we also require the RISC-V toolchain, which includes essential components such as GCC and various build utilities. These components are integral to our comprehensive software stack.

## Slide 11: PoCL: A Performance Portable OpenCL Implementation
Key Insight
  Use target-specific execution model
    SIMT -> GPUs
    MIMD, SIMD -> CPUs
  Target-specific compiler transformations
    Using LLVM
Key Features
  A single interface with multiple target devices
  Support x86, PTX, HASIL export
  Support Custom accelerator support via TCE
OpenCL Program
PoCL
Clang
PoCL Built-in lib
PoCL Devices
(CUDA,TCE …)
PoCL software stack
Notes: Now I will introduce the Vortex PoCL extension, which is designed to enable support for OpenCL programs on the Vortex platform.
PoCL is a project to support executing OpenCL programs on different hardware device.
It is built upon two fundamental insights: the adoption of a target-specific execution model and the implementation of target-specific compiler transformations using LLVM.
Based on key insight, they can support different execution model per device such as GPU and CPU, also they can optimize and generate binary code for specific target.
PoCL extends its support to several backend devices, including x86, NVIDIA GPUs, and custom accelerators.
To execute an opencl programs on a backend device.
First, POCL compiles the program, and link it with hardward dependent runtime library
and also PoCL’s builtin library such as math functions.
Then, the POCL runtime will use the devices runtime functions to control the devices.

## Slide 12: Vortex OpenCL System Architecture
Compilation
  Vortex Kernel
  PoCL Compiler
Execution
  Vortex Runtime
  PoCL Runtime
Vortex Runtime
Vortex Kernel
Notes: The vortex PoCL extension make available compile OpenCL kernel and execute them in the vortex GPU.
we need to care about the following parts: for compilation, we need to modify the POCL Compiler and provide a Vortex Runtime library.
For the Compilation, vortex have different interface as other devices.
thus, we have to modify the original pocl compiler to generate the programs with Vortex ISA.
We also use vortex kernel library in lowering process.
For execution, we need to provide a Vortex runtime for POCL runtime. To integrate a new device into POCL, we have to implement some basic operations, like memory copy, memory allocation and kernel launch and put all these functions into Vortex Runtime. POCL framework will use the Vortex Runitme to control and communicate with Vortex.

## Slide 13: PoCL Vortex Extension
OpenCL kernel
LLVM context Creation
BuiltIn library linking
Workgroup Generation
Device Kernel Translation
Work Schedule Generation
Device Code Generation
PoCL Compiler
OpenCL Application
OpenCL Runtime API
Common Device Interface
CPU & Pthread
PTX
HSA
TCE
Accel
Vortex
Runtime
CPU
GPU
TCE Device
Accel Device
Vortex
GPU
PoCL Runtime
Schedule Generation
  Kernel Invocation
    Warp / thread Scheduling
Device Kernel Translation
  Device runtime library call
Device Code Gen
  Target CPU, features, ABI
  Link libraries such as vortex runtime
Vortex Runtime
  Kernel Translation
  Vortex Driver Communication
    GPU resource allocation and loading
    Kernel offloading and execution
Notes: In summary, vortex software stack need to be integrated into PoCL.
In the right figure, we marked Vortex extension as a orange box.
First, PoCL compiler receive OpenCL kernel and generate program context for target execution model.
Based on the execution model, we insert kernel scheduling code to program context.
we link the vortex kernel library during the device kernel translation
And translate kernel to generate vortex binary.
After got the generated program binary, pocl Runtime uses vortex runtime to offload the kernel to vortex and launch it.

## Slide 14: Compilation and Execution Process
OpenCL kernel
LLVM context Creation
BuiltIn library linking
Workgroup Generation
Device Kernel Translation
Work Schedule Generation
Device Code Generation
PoCL Compiler
OpenCL Application
OpenCL Runtime API
Common Device Interface
CPU & Pthread
PTX
HSA
TCE
Accel
Vortex
Runtime
CPU
GPU
TCE Device
Accel Device
Vortex
GPU
PoCL Runtime
Input: OpenCL programs (host&&kernel)
Step1: Compile OpenCL kernel to risc-v binary (by POCL Compiler)
Step2: Manually edit the host OpenCL programs, to load risc-v binary as kernel.
Step3: Compile edited OpenCL host (by gcc/clang), and link with Vortex Driver.
Step4: Execute compiled OpenCL host programs with POCL Runtime, which loads risc-v binary generated in Step2 as kernel.
Notes: Here is the steps to execute OpenCL.
In this first step, we have to compile the kernel part into risc-v binary. We will use modied POCL compiler in this step.
Since PoCL does not support riscv structure we need to modify pocl compiler to generate binary.

## Slide 15: Compilation and Execution Process
OpenCL kernel
LLVM context Creation
BuiltIn library linking
Workgroup Generation
Device Kernel Translation
Work Schedule Generation
Device Code Generation
PoCL Compiler
OpenCL Application
OpenCL Runtime API
Common Device Interface
CPU & Pthread
PTX
HSA
TCE
Accel
Vortex
Runtime
CPU
GPU
TCE Device
Accel Device
Vortex
GPU
PoCL Runtime
Input: OpenCL programs (host&&kernel)
Step1: Compile OpenCL kernel to risc-v binary (by POCL Compiler)
Step2: Manually edit the host OpenCL programs, to load risc-v binary as kernel.
Step3: Compile edited OpenCL host (by gcc/clang), and link with Vortex Driver.
Step4: Execute compiled OpenCL host programs with POCL Runtime, which loads risc-v binary generated in Step2 as kernel.
Notes: Then, we Manually edit the host OpenCL programs, to load risc-v binary as kernel.

## Slide 16: Compilation and Execution Process
OpenCL kernel
LLVM context Creation
BuiltIn library linking
Workgroup Generation
Device Kernel Translation
Work Schedule Generation
Device Code Generation
PoCL Compiler
OpenCL Application
OpenCL Runtime API
Common Device Interface
CPU & Pthread
PTX
HSA
TCE
Accel
Vortex
Runtime
CPU
GPU
TCE Device
Accel Device
Vortex
GPU
PoCL Runtime
Input: OpenCL programs (host&&kernel)
Step1: Compile OpenCL kernel to risc-v binary (by POCL Compiler)
Step2: Manually edit the host OpenCL programs, to load risc-v binary as kernel.
Step3: Compile edited OpenCL host (by gcc/clang), and link with Vortex Driver.
Step4: Execute compiled OpenCL host programs with POCL Runtime, which loads risc-v binary generated in Step2 as kernel.
Notes: After we generated the binary kernel for our host program. Host code is compiled with the PoCL runtime library which is used for host programs to communicate with Vortex devices.

## Slide 17: Compilation and Execution Process
OpenCL kernel
LLVM context Creation
BuiltIn library linking
Workgroup Generation
Device Kernel Translation
Work Schedule Generation
Device Code Generation
PoCL Compiler
OpenCL Application
OpenCL Runtime API
Common Device Interface
CPU & Pthread
PTX
HSA
TCE
Accel
Vortex
Runtime
CPU
GPU
TCE Device
Accel Device
Vortex
GPU
PoCL Runtime
Input: OpenCL programs (host&&kernel)
Step1: Compile OpenCL kernel to risc-v binary (by POCL Compiler)
Step2: Manually edit the host OpenCL programs, to load risc-v binary as kernel.
Step3: Compile edited OpenCL host (by gcc/clang), and link with Vortex Driver.
Step4: Execute compiled OpenCL host programs with POCL Runtime, which loads risc-v binary generated in Step2 as kernel.
Notes: Finally, we just execute the compiled host programs. It will load the risc-v binary kernel and execute it on Vortex devices by communicating with Vortex driver.

## Slide 18: Mapping from OpenCL Kernel to Vortex
OpenCL processing model
  Work-Item
  Work-Group
  Kernel execution instance
Vortex Work-Items
  Thread
  Wavefront
  Core
Work-Item
Work-Group
Kernel Instance
…
Notes: While compile program for the vortex, one the most important parts is scheduler.
How to map computation to hardware is critical for achieving high performance.
The OpenCL processing model using three terms for specifying processing model, work-item, work-group, and kernel instance.
The work-item specifying the minimal unit of program. The work-group specifying the minimal group of program that processing in the one processing unit.
Instead of work-item and work-group, vortex use wavefront and thread to schedule.
A wavefront is a group of thread and threads within one wavefront are executed in parallel and in lock steps.
In Vortex, we use wavefront as. the unit for scheduling.
The goal of the scheduling is that high-level users can directly execute Vortex without worry about scheduling.
So, we generate scheduling in the compilation process.

## Slide 19: PoCL: Work-group Function Generation
Generate code for executing all work-items in a work group
  Analyze Parallel Region
  Flat Collapsing
    Insert Loop for executing all work-item in a work group
Work-Item
Work A
barrier
Work B
exit
entry
barrier
exit
#work-item
#work-item
entry
Work A
Work B
Analyze Parallel Region
Flat Collapsing
kernel foo(){
doWorkA()
barrier()
doWorkB()
}
Notes: Originally pocl compiler generate work-group function.
PoCL analyze parallel region of the program which can execute parallelly without any sinchronize.
Then insert loop for executing all work-item in a work group, which are called flat collapsing.
Based on the flat collapsing, PoCL can generate code for the CPU.
When we have a kernel function such as left figure.
They find two prallel reiong for work A nad workB by analyze parallel region.
Then perform flat collapsing to generate workgroup function, with generating loop for iterate workA, removing barrier, and generting loop for workB.
Now, work-group function can execute all the work-items.

## Slide 20: Mapping from OpenCL Kernel to Vortex
PoCL work-group function
  Execute All work-items in a work-group
Thread Mapping
  Mapping one work-group to one HW thread
  Distribute work-group among all threads
    All threads: wavefronts * thread
for (all threads) {
}
pocl::wg_func()
for (remaining threads) {
}
pocl::wg_func()
Wavefront 0~N
Wavefront (0)
Notes: With this work-group function, we can simply execute program on the vortex, called thread mapping.
Every thread execute workgroup function, which means mapping one work-group to one hw thread.
The workgroup is distribute among all threads.
Using the given mapping, it is possible that the number of work-groups is not a multiple of the number of threads in a wavefront.
To execute the remaining work-groups, we make the program flow as shown in the right figure, add additional wavefront for dealing remaining work-group.

## Slide 21: LLVM Compiler Extension
New RISCV target feature
Toolchain integration
  GCC toolchain
  Kernel runtime
Assembler/Disassembler
  GPGPU ISA Extension
    Wspawn, tmc, split,join, bar, tex
Optimization Pass
  Divergence Control Pass
    Split/Join auto-insertion
Notes: Furthermore, we have extended the LLVM compiler to generate Vortex ISA code.
Additionally, we integrated the GCC toolchain and kernel runtime into LLVM, and we have enhanced the assembler and disassembler to provide full support for Vortex ISA.
Moreover, we have introduced an optimization pass to manage thread divergence. This pass effectively inserts split and join instructions into regions where divergence occurs.

## Slide 22: Vortex Divergence Control
Handling divergent control-flow
  Divergence analysis
    Mark divergent instructions
  Divergence management
    Insert Split and Join instruction
    Handling loops is more complex
      Use vx_pred to disable threads on conditional
Handling Divergence
  Divergent If/else statement
  Divergent Loops
A
B
C
D
If (threadid.x<2) {
work B
} else {
work C
}
Divergent branch!
Simplification
Notes: To effectively manage divergence, we have introduced both a divergence analysis pass and a management pass.
Through the analysis pass, the optimization pass identify and mark divergent instructions and regions.
Subsequently, the pass strategically insert split and join instructions to handle divergence.
Handling loops bring more complexity when compared to managing divergences compare to other divergence such as if/else constructs.
To address this challenge, we have introduced the vx_pred, allowing us to modify the thread mask based on specified conditions.
The figure in the lower-right corner, it demonstrate how if/else statements can be transformed into split and join instructions based on conditions.
Similarly, when dealing with loops, optimization pass insert split and join instructions at the start and end of the loop while adding vx_pred for condition changes within the loop body.

## Slide 23: Support OpenCL benchmarks with New PoCL
Upgrade PoCL version as 4.0
  Support OpenCL 3.0
  Using llvm vortex based on llvm v16
17 Benchmark support
  Vecadd, sgemm, psort, saxpy, sfilter, nearn, gaussian, dotproduct, kmeans, spmv, cutcp, stencil, lbm, oclprintf, blackscholes, matmul, transpose
    17 benchmarks are fully supported with Mapping 0
Notes: Using this entire opencl pipeline, we can support 17 benchmarks in the rodinia benchmark set.
Currently we use pocl 4.0 with opencl version 3.0 and llvm 16 vortex extension.

## Slide 24: How to use PoCL for the vortex
Detailed instruction for OpenCL pipeline
  https://github.com/vortexgpgpu/pocl/blob/main/README.vortex
Install Dependencies
Build RISC-V GNU toolchain
Build LLVM for Vortex
Build Vortex
Build PoCL compiler for the Vortex
Build PoCL runtime for the Vortex
Notes: For Installing opencl pipeline, The process is relatively straightforward.
You will need to follow these steps:
Begin by installing the necessary dependencies.
Proceed to build the RISC-V GNU toolchain.
Next, compile LLVM-Vortex.
Afterward, compile Vortex.
Lastly, compile both the Pocl compiler and the Pocl runtime.
Detailed instructions can be found on our GitHub repository to ensure a smooth and successful installation process.

## Slide 25: QnA
Thanks for your time!
PoCL compiler for the vortex is an open-source project on Github.
We welcome any kinds of contribution & feedback.
https://github.com/vortexgpgpu/pocl/tree/main
https://github.com/vortexgpgpu/llvm/tree/vortex
https://github.com/vortexgpgpu/vortex
Notes: Thank you for listening.
All of our project are available in the git repository!
We describe a build instruction in the README.vortex file of the pocl github.