## Slide 1: GPGPU Background
Presenter: Hyesoon Kim

## Slide 2: CPU pipeline
CPU pipeline
Increasing the performance in the execution units
  Increase the issue width (superscalar)
  Multi-threading
Memory
Front-end
Decode
Rename
Schedule
Execution
Write-back
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
5-stage pipeline
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
Superscalar
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
F
D
S
E
W
Multi-threading

## Slide 3: GPU pipeline
Warp/Wave-front execution model
SPMD programming model (Single Program Multiple Data)
Inst 1
Inst 2
Inst 3
T1
Inst 1
Inst 2
Inst 3
T2
T3
T4
All threads have the same program
T
T
T
T
One warp
T
T
T
T
Fetch 1 instruction and each instruction has multiple threads are associated.
The group of instruction is called warp/wave-front
Tn
…
T
T
T
T
One warp
T
T
T
T

## Slide 4: GPU Pipeline
Fetch
  One instruction for each warp
  Multiple PC registers exist to support multi-threaded architecture
  Round-robin scheduler
Wide execution width
Scheduler
I-cache
Fetch unit
Decoder
. . . . . .
Memory access unit
. . . . . .
Writeback
Memory
Lane 0
Lane 1
Lane N-1
Lane 0
Lane 1
Lane N-1
Active bit mask vectors/
score boarding
Register
Scheduler (Score boarding)

## Slide 5: Scheduling
In-order scheduler
Inst1 // warp2
warp 2
Inst2 // warp2
Inst1 // warp3
warp 3
Inst2 // warp3
Inst1 // warp4
warp 4
Isnt2 // warp4
warp 1
Inst3
Inst2
Inst1
Inst1 // warp1
Inst2 // warp1
Inst3 // warp2
Inst3 // warp3
Isnt3 //warp4
Inst3 // warp1
(a) Static code
(b) Dynamic instruction trace

## Slide 6: Thread Scheduling Policies
w1
w2
w3
w4
comp_inst1
comp_inst2
mem_inst3
Round-robin
w1
w2
w3
w4
w1
w2
w3
w4
w1
w2
w3
w4
stall
Greedy-then-Oldest (GTO)
w1
w2
w1
w1
M
M
M
M
w1
w2
w3
w4
M
w2
w2
M
w3
w3
w3
M
M
w4
w4
w4
w4
w1
w1
w1
stall

## Slide 7: GPU Register Files
To accommodate a large number of active threads, a large number of register files are essential.
e.g.) 128 threads, 64 registers = 128X64 = 8KB
NVIDIA G80 architecture: 64KB registers (16KB cache)
Vortex: 32-registers # of threads per warp x # of warps x # or cores
Register read BW
1Tflop/s peak performance (2 read, 1 write)
  -2T * 32B/s = 64TB/s register read BW
Highly banked register files

## Slide 8: Register File Structures: Multiple Banks
. . . . . .
. . . . . .
. . . . . .
Register files
. . . . . .
Lane 0
Lane 1
Lane N-1
Warp 0’s reg file
Warp M-1’s reg file
Warp ID.Reg ID
. . .
Th 0
…
Th N-1
Writeback
Multiple banks (Narasiman’s figure)
All threads in a warp read the register values in parallel.
Register is indexed with register ID, warp ID

## Slide 9: Handling Branch Instructions
A reduction example
What about other threads?
What about different paths?
0
1
2
3
4
5
6
7
0
2
4
6
0
4
0
If (threadId.x%==2)
If (threadId.x%==4)
If (threadId.x%==8)
A
B
C
D
If (threadid.x>2) {
do work B}
else {
do work C
}
From Fung et al. MICRO ‘07
Divergent branch!

## Slide 10: Split/Join
Compiler inserts split/join in Vortex
Split:
  Put tmask in the ipdom stack (do work c part}
  Put next PC in the stack (not-taken path. // do work c part )
Join
  Pop from a stack
If (threadid.x>2)
// split
{
do work B
}
else {
// join
do work C
}

## Slide 11: GPGPU Programming
CUDA (Compute Unified Device Architecture)
OpenCL
AMD's HIP
Intel's DPC
OpenMP
And more (RUST etc.)

## Slide 12: Quick Summary of CUDA Programming Model
SIMD or SIMT
  Single instruction multiple data or single instruction multiple thread
Unified Memory space (global memory space)
Program hierarchy
  Thread, block, kernel

## Slide 13: CUDA Program Example

## Slide 14: Execution Model
Thread & Block
Inst 1
Inst 2
Inst 3
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
SM
SM
Shared Memory
SP
SP
SP
SP
Shared Memory
SP
SP
SP
SP
Block
Kernel
Block
warp
warp
warp
Sing instruction multiple thread
Block = a group of thread which share “the shared memory space”
Warp
warp
warp
warp

## Slide 15: Memory Space
 | Space | ~= CPU
Local Memory | Within Threads | Stack
Shared Memory | Within Blocks | Distributed memory space
Global Memory | All | Centralized storage
Constant Memory | All | Centralized read-only storage (very small)
Texture Memory | All | Centralized read-only storage (medium size, 2D- cache)
Thread, block, and kernel have different memory spaces

## Slide 16: Shared Memory
From: http://accel.cs.vt.edu/files/lecture10.pdf

## Slide 17: Memory Data Indexing
SIMT-execution model
Use thread id and block id to index data
Let’s assume N=16, blockDim=4  4 blocks
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
blockIdx.x = 0
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 0,1,2,3
blockIdx.x = 1
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 4,5,6,7
+
blockIdx.x = 2
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 8,9,10,11
blockIdx.x = 3
blockDim.x = 4
threadIdx.x = 0,1,2,3
Idx= 12,13,14,15
+
+
+
+

## Slide 18: 1D, 2D, 3D data structures
A kernel is executed as a grid of thread blocks
Threads and blocks have IDs
  So each thread can decide what data to work on
  Block ID: 1D or 2D
  Thread ID: 1D, 2D, or 3D
Loop index in sequential loop
  Use thread ids, block ids
  1D array index= c1*threadId.x + c2*block Id.x
  2D array index = c1*threadId.x+c2*blockId.x+c3*threadId.y+c4*blockId.y
for (ii = 0; ii < 100; ++ii) {
C[ii] = A[ii] + B[ii];
}
// there are 100 threads
__global__ void KernelFunction(…) {
int tid = blockDim.x * blockIdx.x + threadIdx.x;
int varA = aa[tid];
int varB = bb[tid];
C[tid] = varA + varB;
}
CPU code
CUDA code

## Slide 19: Synchronization Model
Bulk-Synchronous Parallel (BSP) program (Valiant [90])
Synchronization within blocks using explicit barrier
Implicit barrier across kernels
  Kernel 1  Kernel 2
  C.f.) Cuda 3.x
barrier
Block
barrier
Block
barrier
barrier
Block
barrier
Block
barrier
Block
Kernel1
Kernel2
Barrier

## Slide 20: OpenCL vs. CUDA
 | OpenCL | CUDA
Execution Model | Work-groups/work-items | Block/Thread
Memory model | Global/constant/local/private | Global/constant/shared/local + Texture
Memory consistency | Weak consistency | Weak consistency
Synchronization | Synchronization using a work-group barrier (between work-items) | Using synch_threads Between threads