## Slide 1
Using Vortex for Class and Research
https://github.com/vortexgpgpu/vortex_tutorials
Presenter: Hyesoon Kim / Liam Cooper
Notes: 1

## Slide 2
Pre-exercise Setup: VM Download (Recommended)
Install VirtualBox and Vagrant
Download the Vagrant Box image from the tutorial repo
Add and initialize the Box image
Download the Vagrantfile from the tutorial repo
Boot the VM with vagrant up
Finally, run vagrant ssh to connect to VM
Detailed setup instructions in VM_README.md
Test Vortex:
  ./ci/blackbox.sh --cores=2 --app=demo
Notes: 2

## Slide 3
Pre-exercise Setup: Remote Account in Browser
Log into rg-ood.crnch.gatech.edu with provided login
Select the Vortex Tutorial option under the Reconfig tab
Set 2 CPUs and press the Launch button to start a terminal job
Press Connect to open a remote terminal on the server
Detailed setup instructions in REMOTE_ACCESS.md
Test Vortex:
    ./ci/blackbox.sh --cores=2 --app=demo
Notes: 3

## Slide 4
Blackbox
Vortex's main test driver
Arguments
  Clusters, cores, warps, threads
  L2cache, L3cache
  Driver
    rtlsim, vlsim, fpga, simx
  Debug
  Perf
  App
  Args
Arguments
Notes: 4

## Slide 5
6 Tutorial Assignments
Vortex tutorial assignments
  Designed to cover different components of Vortex
  Introduction assignments for RTL: Assignments #1 & #2
  How to modify LSU (lost-store unit) and debug: Assignments #3 & #4
  How to add a custom new instruction: Assignment #5
  Assignments #1 and #2 only explain the steps
  Assignments #3 and #5 provide a solution
https://github.com/vortexgpgpu/vortex_tutorials.git
Notes: 5

## Slide 6
Assignment 1
Add a new performance counter for the average number of active threads per cycle
  Check if instruction is being issued
  Count number of active threads in the active thread mask
  Divide total number of active threads by cycle count in driver
Test with output of demo program kernel
Notes: 6

## Slide 7
Assignment 2
Count the number of coalesced memory requests
  GPUs generate multiple memory requests from the same warp/wave front, often with duplicate memory addresses across multiple threads in the warp
  Increment counter in LSU when memory requests in other threads are the same
  Increment only once per warp
Test with output of demo program kernel
Notes: 7

## Slide 8
Assignment 3/4
Add a simple next line prefetcher in LSU
  Every time a load request is computed, generate the next cache line address and send to d-cache
  Request metadata must be stored somewhere so the processor knows the correct memory requested
Verify implementation by using the debug trace to see if prefetch requests are generated and used correctly
Notes: 8

## Slide 9
Assignment 5
Add a new instruction for prefetching
  Add an intrinsic for the new instruction (to generate a binary with new instruction)
  Define the new instruction in SimX
  Extend the pipeline/decoder
  Modify the LSU to take in prefetch instructions
  Develop a test to check functionality of the new instruction
Debug using kernel dump and run log
Notes: 9

## Slide 10
Checking Solutions for Assignments #3 & #5
Check solutions folder on Github
  Solution overview and code provided
Download and execute solution
  Solution code formatted as git pull requests
  Assignment 3:
    git fetch origin pull/22/head:A3_solution git checkout A3_solution
  Assignment 5:
    git fetch origin pull/25/head:A5_solution git checkout A5_solution
Notes: 10

## Slide 11
Assignment 6
Add Performance counters to test software prefetcher
Measure prefetch metrics
  # of unique prefetch requests
  # of unused prefetched blocks
  # of late prefetches
Notes: 11